## Slide 1: Computer Architecture Experiment
Topic 5. Dynamically Scheduled Pipelines using Scoreboarding
浙江大学计算机学院
2021年9月

## Slide 2: Outline
Experiment Purpose
Experiment Task
Basic Principle
Operating Procedures
Checkpoints

## Slide 3: Experiment Purpose
Understand the principle of piplines that support multicycle operations.
Understand the principle of Dynamic Scheduling With a Scoreboard.
Master the design methods of piplines that support multicycle operations.
Master the design methods of Dynamically Scheduled Pipelines using Scoreboarding.
Master verification methods of Dynamically Scheduled Pipelines using Scoreboarding.

## Slide 4: Experiment Task
Redesign the pipelines with IF/IS/RO/FU/WB stages and supporting multicycle operations.
Design of a scoreboard and integrate it to CPU.
Verify the Pipelined CPU with program and observe the execution of program.

## Slide 6: Instr. Mem.(1)
NO. | Instruction | Addr. | Label | ASM | Comment
0 | 00000013 | 0 | __start: | addi x0, x0, 0 | 
1 | 00402103 | 4 |  | lw x2, 4(x0) | 
2 | 00802203 | 8 |  | lw x4, 8(x0) | Structural Hazard
3 | 004100b3 | C |  | add x1, x2, x4 | 
4 | fff08093 | 10 |  | addi x1, x1, -1 | WAW
5 | 00c02283 | 14 |  | lw x5, 12(x0) | 
6 | 01002303 | 18 |  | lw x6, 16(x0) | 
7 | 01402383 | 1C |  | lw x7, 20(x0) | 
8 | 402200b3 | 20 |  | sub x1,x4,x2 | 
9 | ffd50093 | 24 |  | addi x1,x10,-3 | 
10 | 00520c63 | 28 |  | beq x4,x5,label0 | 
11 | 00420a63 | 2C |  | beq x4,x4,label0 | 
12 | 00000013 | 30 |  | addi x0,x0,0 | 
13 | 00000013 | 34 |  | addi x0,x0,0 | 
14 | 00000013 | 38 |  | addi x0,x0,0 | 

## Slide 7: Instr. Mem.(2)
NO. | Instruction | Addr. | Label | ASM | Comment
15 | 00000013 | 3C |  | addi x0,x0,0 | 
16 | 000040b7 | 40 | label0: | lui x1,4 | 
17 | 00c000ef | 44 |  | jal x1,12 | 
18 | 00000013 | 48 |  | addi x0,x0,0 | 
19 | 00000013 | 4C |  | addi x0,x0,0 | 
20 | ffff0097 | 50 |  | auipc x1, 0xffff0 | 
21 | 0223c433 | 54 |  | div x8, x7, x2 | 
22 | 025204b3 | 58 |  | mul x9, x4, x5 | 
23 | 022404b3 | 5C |  | mul x9, x8, x2 | St. Ha./RAW/WAW
24 | 00400113 | 60 |  | addi x2, x0, 4 | WAR
25 | 000000e7 | 64 |  | jalr x1,0(x0) | 
26 | 00000013 | 68 |  | addi x0,x0,0 | 
27 | 00000013 | 6C |  | addi x0,x0,0 | 

## Slide 8: Data Mem.
NO. | Data | Addr. | Comment
0 | 000080BF | 0 | 
1 | 00000008 | 4 | 
2 | 00000010 | 8 | 
3 | 00000014 | C | 
4 | FFFF0000 | 10 | 
5 | 0FFF0000 | 14 | 
6 | FF000F0F | 18 | 
7 | F0F0F0F0 | 1C | 
8 | 00000000 | 20 | 
9 | 00000000 | 24 | 
10 | 00000000 | 28 | 
11 | 00000000 | 2C | 
12 | 00000000 | 30 | 
13 | 00000000 | 34 | 
14 | 00000000 | 38 | 
15 | 00000000 | 3C | 
NO. | Instruction | Addr. | Comment
16 | 00000000 | 40 | 
17 | 00000000 | 44 | 
18 | 00000000 | 48 | 
19 | 00000000 | 4C | 
20 | A3000000 | 50 | 
21 | 27000000 | 54 | 
22 | 79000000 | 58 | 
23 | 15100000 | 5C | 
24 | 00000000 | 60 | 
25 | 00000000 | 64 | 
26 | 00000000 | 68 | 
27 | 00000000 | 6C | 
28 | 00000000 | 70 | 
29 | 00000000 | 74 | 
30 | 00000000 | 78 | 
31 | 00000000 | 7C | 

## Slide 9: Test Bench
RV32core core(
.debug_en(1'b0),
.debug_step(1'b0),
.debug_addr(7'b0),
.debug_data(),
.clk(clk),
.rst(rst),
.interrupter(1'b0)
);
initial begin
clk = 0;
rst = 1;
#2 rst = 0;
end
always #1 clk = ~clk;

## Slide 10: Simulation (1)

## Slide 11: Simulation (2)

## Slide 12: Simulation (3)

## Slide 13: Simulation (4)

## Slide 14: Simulation (5)

## Slide 15: Simulation (6)

## Slide 16: Simulation (7)

## Slide 17: Simulation (8)

## Slide 18: Checkpoints
CP 1:
  Waveform Simulation of the Pipelined CPU with the verification program
CP 2:
  FPGA Implementation of the Pipelined CPU with the verification program

## Slide 19
Thanks!