## Slide 1: Computer Architecture ----A Quantitative Approach
陈文智
浙江大学计算机学院
chenwz@zju.edu.cn

## Slide 2: What is Pipelining ?
Pipelining:
  “A technique designed into some computers to increase speed by starting the execution of one instruction before completing the previous one.”
  ----Modern English-Chinese Dictionary
  implementation technique whereby different instructions are overlapped in execution at the same time.
  implementation technique to make fast CPUs

## Slide 3: Why Pipelining: Its Natural
Laundry
  Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, and fold
  Washer takes 30 minutes
  Dryer takes 40 minutes
  “Folder” takes 20 minutes
A
B
C
D

## Slide 4: Sequential Laundry
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
Time
T
a
s
k
O
r
d
e
r

## Slide 5: Pipelined Laundry----Start work ASAP
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 6: Why pipelining : overlapped
Latches, called pipeline registers’ break up computation into 5 stages
Deal 5 tasks at the same time.
Only deal one task each time.
This task takes
“ such a long time”

## Slide 7: Why pipelining: more faster
Can “launch” a new computation every 100ns in this structure
Can finish 107 computations per second
Can launch a new computation every 20ns in pipelined structure
Can finish 5×107 computations per second

## Slide 8: Why pipelining : conclusion
The key implementation technique used to Make fast CPU: decrease CPUtime.
Improving of Throughput ( rather than individual execution time)
Improving of efficiency for resources (functional unit)

## Slide 9: What is a pipeline ?
A pipeline is like an auto assemble line
A pipeline has many stages
Each stage carries out a different part of instruction or operation
The stages, which cooperates at a synchronized clock, are connected to form a pipe
An instruction or operation enters through one end and progresses through the stages and exit through the other end
Pipelining is an implementation technique that exploits parallelism among the instructions in a sequential instruction stream

## Slide 10: Ideal Performance for Pipelining
If the stages are perfectly balanced, The time per instruction on the pipelined processor equal to:
Time per instruction on unpipelined machine
Number of pipe stages
So, Ideal speedup equal to
Number of pipe stages.

## Slide 11: Why not just make a 50-stage pipeline ?
Some computations just won’t divide into any finer (shorter in time) logical implementation.
5 stages OK
50 stages NO. Sorry!

## Slide 12: Why not just make a 50-stage pipeline ?
Those latches are NOT free, they take up area, and there is a real delay to go THRU the latch itself.
  Machine cycle > latch latency + clock skew
In modern, deep pipeline (10-20 stages), this is a real effect
Typically see logic “depths” in one pipe stage of 10-20 “gates”.
At these speeds, and with this few levels of logic, latch delay is important

## Slide 13: How Many Pipeline Stages?
E.g., Intel
  Pentium III, Pentium 4: 20+ stages
  More than 20 instructions in flight
  High clock frequency (>1GHz)
  High IPC
Too many stages:
  Lots of complications
  Should take care of possible dependencies among in-flight instructions
  Control logic is huge

## Slide 14: Single-cycle implementation
seldom used !

## Slide 15: Multi-cycle implementation

## Slide 16: Optimized Multi-cycle implementation
Temporary storage locations

## Slide 17: 5-stage Version of MIPS Datapath
store
load
pipeline
registers or
latches

## Slide 18: Single-cycle implementation vs. pipelining
Load
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Store
IF
ID
EX
MEM
WB
R-type
Single Cycle Implementation: CPI=1, long clock cycle
Clk
Load
Store
Waste
Cycle 1
Cycle 2
Pipeline Implementation: CPI=1, clock cycle  long clock cycle/5
Clk
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10

## Slide 19: Multi-cycle implementation vs. pipelining
Load
Store
R-type
Clk
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Clk
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Cycle 9
Cycle 10
Multip-Cycle Implementation: CPI=5,
Pipeline Implementation: CPI=1,
Load
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Store
IF
ID
EX
MEM
WB
R-type
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB

## Slide 20: How simple as this ! Really ?
store
load
pipeline
registers or
latches
Why need to add this line?

## Slide 21: Pipeline hazard: the major hurdle
A hazard is a condition that prevents an instruction in the pipe from executing its next scheduled pipe stage
Taxonomy of hazard
  Structural hazards
    These are conflicts over hardware resources.
  Data hazards
    Instruction depends on result of prior computation which is not ready (computed or stored) yet
  Control hazards
    branch condition and the branch PC are not available in time to fetch an instruction on the next clock

## Slide 22: Hazards can always be resolved by Stall
The simplest way to "fix" hazards is to stall the pipeline.
Stall means suspending the pipeline for some instructions by one or more clock cycles.
The stall delays all instructions issued after the instruction that was stalled, while other instructions in the pipeline go on proceeding.
A pipeline stall is also called a pipeline bubble or simply bubble.
No new instructions are fetched during a stall .

## Slide 23: Performance of pipeline with stalls
Pipeline stalls decrease performance from the ideal
Recall the speedup formula:

## Slide 24: Case of multi-cycle implementation
The ideal CPI on a pipelined processor is almost always 1. (may less than or greater that )
So
Ignore the overhead of pipelining clock cycle.
Pipe stages are ideal balanced.

## Slide 25: Case of multi-cycle implementation
So: Clock cycle unpipelined = Clock cycle pipelining
CPl unpipelined = pipeline depth

## Slide 26: Case of single-cycle implementation
CPI unpipelined = 1
 Clock cycle pipelined =
Clock cycle unpipelined
pipeline depth

## Slide 27: Structural hazard: Pipe Stage Contention
Structural hazards
  Occurs when two or more instructions want to use the same hardware resource in the same cycle
  Causes bubble (stall) in pipelined machines
  Overcome by replicating hardware resources
    Multiple accesses to the register file
    Multiple accesses to memory
    some functional unit is not fully pipelined.
    Not pipelined functional units

## Slide 28: Problems that pipelining introduces
Focus: different operations with the same data path resource on the same clock cycle is not possible. (structure hazard)
There is conflict about the memory !
Mem
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Ld/St
Instr 1
Instr 2
Instr 3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Reg
Mem
Reg

## Slide 29: Insert Stall
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Ld/St
Instr 1
Instr 2
Instr 3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Bubble
Bubble
Bubble
Bubble
Bubble
Stall

## Slide 30: Separate instruction and data memories
Let’s split instruction and data cache
the memory system must deliver 5 times the bandwidth over the unpipelined version.
IM
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Ld/St
Instr 1
Instr 2
Instr 3
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
Reg
DM
Reg

## Slide 31: Multi access to the register file
Simply insert a stall , speedup will be decreased.
We have resolved it with “ double bump”

## Slide 32: Sometimes we can redesign the resource
allow WRITE-then-READ in one clock cycle (double pump)
  Two reads and one write required per clock.
  Need to provide two read port and one write port.
What happens when a read and a write occur to the same register ? ( Data hazard )

## Slide 33: Not fully pipelined function unit : may cause structural hazard

## Slide 34: Machine without structural hazards will always have a lower CPI
Example (pA-14)
  Data reference constitute 40% of the mix
  Ideal CPI ignoring the structural hazard is 1
  The processor with the structural hazard has a clock rate that is 1.05 times higher than that of a processor without structural hazard.
Answer
  Average instruction time = CPIClock cycle time
  =(1+0.4 1) CCideal/1.05
  = 1.3  CCideal
  Clearly, the processor without the structural hazard is faster.

## Slide 35: Why allow machine with structural hazard ?
To reduce cost.
  i.e. adding split caches, requires twice the memory bandwidth.
  also fully pipelined floating point units costs lots of gates.
  It is not worth the cost if the hazard does not occur very often.
To reduce latency of the unit.
  Making functional units pipelined adds delay
  (pipeline overhead -> registers.)
  An unpipelined version may require fewer clocks per operation.
  Reducing latency has other performance benefits, as we will see.

## Slide 36: Example: impact of structural hazard to performance
Example
  Many machines have unpipelined float-point multiplier.
  The function unit time of FP multiplier is 6 clock cycles
  FP multiply has a frequency of 14% in a SPECfp benchmark
  Will the structural hzard have a large performance impact on the SPECfp benchmark?

## Slide 37: Answer to the example
In the best case: FP multiplies are distributed uniformly.
  There is one multiply in every 7 clock. 1/14%
  Then there will be no structural hazard, then there is no performance penalty at all.
In the worst case: the multiplies are all clustered with no intervening instructions.
  Then every multiply instruction have to stall 5 clock cycles to wait for the multiplier be released.
  The CPI will increase 70% to 1.7, if the ideal CPI is 1.
Experiment result:
  This structural hazard increase execution time by less than 3%.

## Slide 38: Data hazard
Data hazards occur when the pipeline changes the order of read/write accesses to operands comparing with that in sequential executing .
Let’s see an Example
  DADD R1, R1, R3
  DSUB R4, R1, R5
  AND R6, R1, R7
  OR R8, R1, R9
  XOR R10, R1, R11

## Slide 39: Coping with data hazards:example

## Slide 40: Data hazard
Basic structure
  An instruction in flight wants to use a data value that’s not “done” yet
  “Done” means “it’s been computed” and “it’s located where I would normally expect to go look in the pipe hardware to find it”
Basic cause
  You are used to assuming a purely sequential model of instruction execution
  Instruction N finishes before instruction N+k, for k >= 1
  There are dependencies now between “nearby” instructions (“near” in sequential order of fetch from memory)
Consequence
  Data hazards -- instructions want data values that are not done yet, or in the right place yet

## Slide 41: Somecases “Double Bump” can do !

## Slide 42: Proposed solution
Proposed solution
  Don’t let them overlap like this…?
Mechanics
  Don’t let the instruction flow through the pipe
  In particular, don’t let it WRITE any bits anywhere in the pipe hardware that represents REAL CPU state (e.g., register file, memory)
  Let the instruction wait until the hazard resolved.
  Name for this operation: PIPELINE STALL
  SLOW！

## Slide 43: Forwarding: reduce data hazard stalls
If the result you need does not exist AT ALL yet,
  you are out of luck, sorry.
But, what if the result exists, but is not stored back yet?
  Instead of stalling until the result is stored back in its “natural” home…
  grab the result “on the fly” from “inside” the pipe, and send it to the other instruction (another pipe stage) that wants to use it

## Slide 44: Forwarding
Generic name: forwarding ( bypass, short-circuiting)
  Instead of waiting to store the result, we forward it immediately (more or less) to the instruction that wants it
  Mechanically, we add buses to the datapath to move these values around, and these buses always “point backwards” in the datapath, from later stages to earlier stages

## Slide 45: Forwarding: reduce data hazard stalls
Data may be already computed - just not in the Register File
EX/MEM.ALUoutput  ALU input port
MEM/WB.ALUoutput  ALU input port

## Slide 46: Hardware Change for Forwarding
MEM/WR
ID/EX
EX/MEM
Data
Memory
ALU
mux
mux
Registers
NextPC
Immediate
mux
EX/Mem.ALUoutput  ALU input
MEM/WB.ALUoutput  ALU input
MEM/WB.LMD  ALU input

## Slide 47: Forwarding path to other input entry
store
load
MEM/WB.LMD  DM input

## Slide 48: Forwarding Doesn’t Always Work

## Slide 49: So we have to insert stall: Load stall
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
Reg
ALU
DMem
Ifetch
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Ifetch
ALU
DMem
Reg
Bubble
Reg
Ifetch
ALU
DMem
Bubble
Reg
or r8,r1,r9

## Slide 50: How to implement Load Interlock
Detect when should use Load Interlock
situation | Example code sequence | Action
No dependence | LD R1, 45(R2) DADD R5,R6,R7 DSUB R8,R6,R7 OR R9,R6,R7 | No hazard possible because of no dependence
Dependence requiring stall | LD R1, 45(R2) DADD R5,R1,R7 DSUB R8,R6,R7 OR R9,R6,R7 | Comparators detect the use of R1 in the DADD and stall the DADD (and DSUB and OR ) before the DADD begins EX
Dependence overcome by forwarding | LD R1, 45(R2) DADD R5,R6,R7 DSUB R8,R1,R7 OR R9,R6,R7 | Comparators detect the use of R1 in DSUB and forward result of load to ALU in time for DSUB to begin EX
Dependence with accesses in order | LD R1, 45(R2) DADD R5,R6,R7 DSUB R8,R6,R7 OR R9,R1,R7 | No action required because read of R1 by OR occurs in the second half of the ID phase, while the write of the loaded data occurred in the first half.

## Slide 51: The logic to detect for Load interlock
Opcode field of ID/EX | Opcode Field of IF/ID | Matching operand fields
Load | Reg-Reg ALU | ID/EX.IR[rt]==IF/ID.IR[rs]
Load | Reg-Reg ALU | ID/EX.IR[rt]==IF/ID.IR[rt]
Load | Load,store, ALU immediate, branch | ID/EX.IR[rt]==IF/ID.IR[rs]

## Slide 52: Example of Forwarding and Load Delay
Why forwarding?
  ADD R4, R5, R2
  LW R15, 0(R4)
  SW R15, 4(R2)
Why load delay?
  ADD R4, R5, R2
  LW R15, 0(R4)
  SW R15, 4(R2)

## Slide 53: Solution (without forwarding)

## Slide 54: Solution (with forwarding)

## Slide 55: The performance influence of load stall
Example
  Assume 30% of the instructions are loads.
  Half the time, instruction following a load instruction depends on the result of the load.
  If hazard causes a single cycle delay, how much faster is the ideal pipeline ?
Answer
  CPI = 1+30%50% 1=1.15
  The performance decrease about 15% due to load stall.

## Slide 56: Fraction of load that cause a stall
Chart: Fraction of loads that cause a stall
| compress | eqntott | espresso | gcc | li | doduc | ear | hydro2d | mdijdp | su2cor
Fraction of loads that cause a stall | 0.24 | 0.41 | 0.12 | 0.23 | 0.24 | 0.2 | 0.2 | 0.1 | 0.1 | 0.04

## Slide 57: Instruction reordering by compiler to avoid load stall
Try producing fast code for
a = b + c;
d = e – f;
assuming a, b, c, d ,e, and f in memory.
Slow code:
LW Rb,b
LW Rc,c
ADD Ra,Rb,Rc
SW a,Ra
LW Re,e
LW Rf,f
SUB Rd,Re,Rf
SW d,Rd
Fast code:
LW Rb,b
LW Rc,c
LW Re,e
ADD Ra,Rb,Rc
LW Rf,f
SW a,Ra
SUB Rd,Re,Rf
SW d,Rd

## Slide 58: The Control hazard
Cause
  branch condition and the branch PC are not available in time to fetch an instruction on the next clock
  The next PC takes time to compute
  For conditional branches, the branch direction takes time to compute.
Control hazards can cause a greater performance loss for MIPS pipeline than do data hazards.

## Slide 59: Recall: solve the hazard by inserting stalls
48 or 72
24

## Slide 60: The pipeline status
Branch instruction | IF | ID | EX | MEM | WB |  | 
Branch Successor |  | IF | stall | stall | idle | idle | 
Branch successor+1 |  |  |  |  | IF | ID | EX
Branch successor+2 |  |  |  |  |  | IF | ID
Branch successor+3 |  |  |  |  |  |  | IF

## Slide 61: Flushing the pipeline
Simplest hardware:
  Holding or deleting any instruction after branch until the branch destination is know.
  Penalty is fixed.
  Can not be reduced by software.

## Slide 62: Stalls greatly hurt the performance
Problem:
  With a 30% branch frequency and an ideal CPI of 1, how much the performace is by inserting stalls ?
Answer:
  CPI = 1+30%３＝1.9
  this simple solution achieves only about half of the ideal performance.

## Slide 63: Move the Branch Computation Forward

## Slide 64: Move the Branch Computation more Forward
store
load

## Slide 65: Why “waste” the fetched instruction ?
We have fetched the instruction 48, why we fetch the second time if the branch not taken at last ?
48 or 72

## Slide 66: Delayed branch
Good news
  Just 1 cycle to figure out what the right branch address is
  So, not 2 or 3 cycles of potential NOP or stall
Strange news
  OK, it’s always 1 cycle, and we always have to wait
  And on MIPS, this instruction always executes, no matter whether the branch taken or not taken. (hardware scheme)

## Slide 67: Branch delay slot
Hence the name: branch delay slot
  The instruction cycle after the branch is used for address calculation , 1 cycle delay necessary
  SO…we regard this as a free instruction cycle, and we just DO IT
Consequence
  You (or your compiler) will need to adjust your code to put some useful work in that “slot”, since just putting in a NOP is wasteful (compiler scheme)

## Slide 68: How to adjust the codes?

## Slide 69: Example: rewrite the code (a)

## Slide 70: Example: rewrite the code (b-1)
Loop: LW R2, 0(R1)
ADD R3, R2, R4
SW R3, 0(R1)
……
SUB R1, R1, #4
BNEZ R1, Loop
LW R2, 0(R1)
Loop: ADD R3, R2, R4
SW R3, 0(R1)
……
SUB R1,R1, #4
BNEZ R1, Loop
LW R2, 0(R1)

## Slide 71: Example: rewrite the code (b-2)
Loop: LW R2, 0(R1)
ADD R3, R2, R4
SW R3, 0(R1)
DIV …..
……
SUB R1, R1, #4
BNEZ R1, Loop
Loop: LW R2, 0(R1)
ADD R3, R2, R4
DIV …...
…...
SUB R1, R1, #4
BNEZ R1, Loop
SW R3, +4(R1)

## Slide 72: Extending the MIPS pipeline to handle MultiCycle Operations
Alternative resolutions to handle floating-point operations
  Complete operation in 1 or 2 clock cycles,
    Which means using a slow clock,
    or/and using enormous amounts of logic in FP units.
  Allow for a longer latency for operations
    The EX cycle may be repeated as many times as needed to complete the operation
    There may be multiple FP units

## Slide 73: MIPS pipeline with FP units

## Slide 74: Pipelining some of the FP units
Two terminologies
  Latency---the number of intervening cycles between an instruction that produces a result and an instruction that uses the result.
  Initiation interval---the number of cycles that must elapse between instructions issue to the same unit.
    For full pipelined units, initiation interval is 1
    For unpipelined units, initiation interval is always the latency plus 1.

## Slide 75: Latencies and initiation intervals for functional units

## Slide 76: Pipeline supports multiple outstanding FP operations

## Slide 77: Specifications
Memory bandwidth: double words/one cycle
New pipeline latches are required:
  M1/M2, M2/M3, M3/M4, M4/M5, M5/M6, M6/M7
  A1/A2, A2/A3, A3/A4
New connection registers are required:
  ID/EX, ID/M1, ID/A1, ID/DIV
  EX/MEM, M7/MEM, A4/MEM, DIV/MEM
Because the divider unit is unpipelined, structural hazards can occur.
Because the instructions have varying running times, the number of register writes required in a cycle can be larger than 1
New data hazards: WAW is possible due to disorder WBs
Due to longer latency of operations, stalls for RAW hazards will be more frequent.
Problems with exceptions resulting from disorder completion

## Slide 78: Issuing in order and completion out of order

## Slide 79: Structural Hazards for the FP register write port

## Slide 80: How to solve the write port conflict ?
Increase the number of write ports
  Unattractive at all !
  No worthy since steady state usage is close to 1.
Detect and insert stalls by serializing the writes
  Track the use of the write port in the ID stage and to stall an instruction before it issues
    Additional Hardware: a shift register+ write conflict logic
    The shift register tracks when already-issued instructions will use the register file, and right shift 1 bit each clock.
    The stalls might aggravate the data hazards
    All interlock detection and stall insertion occurs in ID stage
  To stall a conflicting instruction when it tries to enter the MEM or WB stage.
    Easy to detect the conflict at this point
    Complicates pipeline control since stalls can now occur in two places.

## Slide 81: Types of data hazards
Consider two instructions, A and B. A occurs before B.
RAW( Read after write) true dependence
  Instruction A writes Rx，instruction B reads Rx
WAW(Write after write) output dependence
  Instruction A writes Rx，instruction B writes Rx
WAR( Write after read) anti-denpendence
  Instruction A reads Rx，instruction B writes Rx
Hazards are named according to the ordering that MUST be preserved by the pipeline

## Slide 82: RAW dependence
B tries to read a register before A has written it and gets the old value.
This is common, and forwarding helps to solve it.
S(A)
D(A)
S(B)
D(B)
Time
No hazard
S(A)
D(A)
S(B)
D(B)
If D(A)=S(B), hazard occur.

## Slide 83: WAW dependence
B tries to write an operand before A has written it.
After instruction B has executed, the value of the register should be B's result, but A's result is stored instead.
This can only happen with pipelines that write values in more than one stage, or in variable-length pipelines (i.e. FP pipelines).
S(A)
D(A)
S(B)
D(B)
Time
No hazard
S(A)
D(A)
S(B)
D(B)
If D(A)=D(B), hazard occur.

## Slide 84: WAR dependence
B tries to write a register before A has read it.
In this case, A uses the new (incorrect) value.
This type of hazard is rare because most pipelines read values early and write results late.
However, it might happen for a CPU that had complex addressing modes. i.e. autoincrement.
S(A)
D(A)
S(B)
D(B)
Time
No hazard
S(B)
D(B)
If S(A)=D(B), hazard occur.
S(A)
D(A)

## Slide 85: Stalls arising from RAW hazards

## Slide 86: The WAW hazards

## Slide 87: Solving the WAW hazard
Stall an instruction that would "pass" another until after the earlier instruction reaches the MEM phase.
Cancel the WB phase of the earlier instruction
Both of these can be done in ID, i.e. when LD is about to issue.
Since pure WAW hazards are not common, either method works.
Pick the one that simplest to implement.
The simplest solution for the MIPS pipeline is to hold the instruction in ID if it writes the same register as an instruction already issued.

## Slide 88: What other hazards are possible ?
Hazards among FP instructions.
Hazards between an FP instruction and an integer instruction.
  Since two register files exist, only FP loads and stores and FP register moves to integer registers involve hazards.

## Slide 89: Checks are required in ID
Check for structural hazards
  The divide unit and Register write port.
Check for RAW hazards
  The CPU simply stalls the instruction at ID stage until:
    Its source registers are no longer listed as destinations in any of the execution pipeline registers (registers between stages of M and A) OR
    Its source registers are no longer listed as the destination of a load in the EX/MEM register.
Check for WAW hazards
  Check instructions in A1, ..., A4, Divide, or M1, ...,M7 for the same destination register (check pipeline registers.)
  Stall instruction in ID if necessary.

## Slide 90: Performance of MIPS FP pipeline

## Slide 91: Performance of MIPS FP pipeline

## Slide 92: The MIPS R4000 pipeline
IF－First half of instruction fetch. PC selection occurs. Cache access is initiated.
IS－Second half of instruction fetch.
－This allows the cache access to take two cycles.
RF－Decode and register fetch, hazard checking, I-cache hit detection.
EX－Execution: address calculation, ALU Ops, branch target calculation and condition evaluation.
DF/DS/TC
  － Data fetched from cache in the first two cycles.
  － The third cycle involves checking a tag check to determine if the cache access was a hit.
WB－Write back result for loads and R-R operations.

## Slide 93: Possible stalls and delays
Load delay: two cycles
  The delay might seem to be three cycles, since the tag isn't checked until the end of the TC cycle.
  However, if TC indicates a miss, the data must be fetched from main memory and the pipeline is backed up to get the real value.

## Slide 94: Load stalls

## Slide 95: Example：load stalls

## Slide 96: Branch delay: three cycles
Branch delay: three cycles (including one branch delay slot)
  The branch is resolved during EX, giving a 3 cycle delay.
  The first cycle may be a regular branch delay slot (instruction always executed) or a branch-likely slot (instruction cancelled if branch not taken).
  MIPS uses a predict-not-taken method presumably because it requires the least hardware.

## Slide 97: Branch Delays： 3 stalls

## Slide 98: Pipeline status for branch latency

## Slide 99: The FP 8-stage operational pipeline

## Slide 100: Latency and initiation intervals

## Slide 101: Structural hazards-1

## Slide 102: Structural hazards-2

## Slide 103: Structural hazards-3

## Slide 104: Structural hazards-4

## Slide 105: Performance loss measurements

## Slide 106
THANK YOU
THANK YOU